## Slide 1: Microarchitectural Side-Channel Attacks
Yuval Yarom
The University of Adelaide and Data61

## Slide 2: Publications on microarchitectural timing attacks
Data from [GYCH16]

## Slide 3: Publications and Global Temperature

## Slide 4: Global Average Temperatures Vs. Number of Pirates
Image from :http://sparrowism.soc.srcf.net/home/pirates.html

## Slide 5: Pirates and publications on microarchitectural timing attacks
Pirate image By J.J. at the English language Wikipedia, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=665628

## Slide 6: Still considered hard
OpenSSL
    LOW Severity. This includes issues such as those that … or hard to exploit timing (side channel) attacks.
  https://www.openssl.org/policies/secpolicy.html
At the same time
  Publications are terse – technical details are often omitted
  Generic tools do not exist

## Slide 7: Still considered hard
OpenSSL
    LOW Severity. This includes issues such as those that … or hard to exploit timing (side channel) attacks.
  https://www.openssl.org/policies/secpolicy.html
Attacks are easy, but at the same time
  Publications are terse – technical details are often omitted
  Generic tools do not exist

## Slide 8: Motivation
Reduce barriers to entry
Why?
  Offensive research
    A potential leak is nice. An exploit is better
  Cipher development
    Know your enemy
How?
  Education – this tutorial
  Tools – Mastik

## Slide 9: Mastik
Extremely bad acronym for Micro-Architectural Side-channel ToolKit
Aims
  Collate information on SC attacks
    Improve our understanding of the domain
    Provide somewhat-robust implementations of all known SC attack techniques for every architecture
    Implementation of generic analysis techniques
  Overcome the barrier to entry into the area
  Shift focus to cryptanalysis

## Slide 10: Mastik - Status
Reasonably solid implementation of four attacks
  Prime+Probe on L1-D, L1-I and L3, Flush+Reload
Only Intel x86-64, on Linux and Mac
  x86-32 and limited ARM currently working in the lab
Zero documentation, little testing
No user feedback

## Slide 11: Outline
Background on and a taxonomy of microarchitectural side-channel attacks
The Flush+Reload attack and variants
The Prime+Probe attack
Countermeasures
Slides and sources available at http://cs.adelaide.edu.au/~yval/CHES16/

## Slide 12: The Microarchitecture
An (Instruction Set) Architecture (ISA) can have multiple implementations
  A microarchitecture is one such implementation
  The ISA abstracts the implementation detail
The microarchitecture is functionally transparent
  But contains hidden state that can be observed through program execution timing

## Slide 13: The Microarchitecture
ISA
Software
Hardware
Image adapted from [GYCH16]

## Slide 14: The Microarchitecture
An (Instruction Set) Architecture (ISA) can have multiple implementations
  A microarchitecture is one such implementation
  The ISA abstracts the implementation detail
The microarchitecture is functionally transparent
But contains hidden state that can be observed through program execution timing

## Slide 15: Microarchitectural attacks
Create contention on microarchitectural components
Which results in timing variations
That are used to expose an intarnal state
Which depends on secret data
Allowing the attacker to infer said data

## Slide 16: Attack taxonomy - level
ISA
Software
Hardware
Core shared
Package shared
System shared
Image adapted from [GYCH16]

## Slide 17: Attack taxonomy – type [AS07]
Persistent-state attacks
  Spatial contention on limited storage space
  Example: most cache attacks
Transient-state attacks
  Temporal contention on limited processing speed
  Example: CacheBleed

## Slide 18: Basic taxonomy
We focus on persistent-state at the package level (with some core)
 | Persistent-state | Transient-state
Core level | [Ber05,Per05, OST06] Others | [Lam73,Ber05, AS07,YGH16]
Package | [YF14,LYG+15,IES15] | ?
System | [PGM+16,IES16] | [WS12,WXW12]

## Slide 19: Other classifications
Classical taxonomy [Pag03], [NS06]
  Time-driven – measure complete execution time
  Trace-driven – capture sequence of cache hits/misses
  Access-driven – obtain some information on accessed memory addresses
Internal vs. external contention [AK09]
Degree of concurrency [GYCH16]
  Multicore
  Hyperthreading
  Time slicing

## Slide 20: History
Lampson [Lam73]
  Defines covert channels
  Suggests the first micro-architectural timing channel:

## Slide 21: History
Page [Pag02] – First theoretical cache-based attack
Tsunoo et al. [TTMM02] – First microarchitectural side-channel attack
  Cache-based timing attack on Misty
    Mostly forgotten
Tsunoo et al. [TSS+03]
  Cache-based timing attack on DES

## Slide 22: The (X86) Cache
Memory is slower than the processor
The cache utilises locality to bridge the gap
  Divides memory into lines
  Stores recently used lines
Shared caches improve performance for multi-core processors
Processor
Memory
Cache
Notes: Another thing that changed since my Apple // days is the processor speed. My apple 2 ran at 1 MHz. My mac runs at 2GHz. Memory speed, however, has not fared so well. The memory on my apple needed half a clock cycle to produce data, whereas modern computers require about 200. When the processor reads from memory it needs to wait. <click> and if it needs to read from the same location again it needs to wait again. <click>. So, we have a speed gap between the processor and the memory.
The cache is the part of the processor that bridges this gap. It is a small memory that is included within the processor. Being small, being closer to the execution core and using more expensive technologies than the main memory mean that the cache is much faster than the memory. On intel the spead ranges from 4 to 50 cycles, depending on the level of cache.
Yada yada

## Slide 23: Cache Consistency
Memory and cache can be in inconsistent states
  Rare, but possible
Solution: Flushing the cache contents
  Ensures that the next load is served from the memory
Processor
Memory
Cache

## Slide 24: The Flush+Reload Technique
Exploits cache behaviour to leak information on victim access to shared memory.
Spy monitors victim’s access to shared code
  Spy can determine what victim does
  Spy can infer the data the victim operates on

## Slide 25: Detour - Virtual Memory
Processes execute within a virtual address space
  Virtual pages map to physical frames

## Slide 26: Sharing
Frames can be shared by multiple processes
  Read only sharing maintains functional isolation
  Protection using Copy-on-write

## Slide 27: Causes of sharing
Content-aware sharing
  Pages from the same file have identical content
  Shared program or library code
    Can also share constant data
  Shared images in PaaS clouds
Content-based sharing (a.k.a. page deduplication)
  The system identifies and coalesces identical pages
  Implemented in many hypervisors and in most modern operating systems

## Slide 28: Flush+Reload [GBK11,YF14]
Flush memory line
Wait a bit
Measure time to Reload line
  slow-> no access
  fast-> access
Repeat
Processor
Memory
Cache
Notes: Reminder: Fast 50 cycles. Slow 200. Measurement adds about 30 cycles.
Wrap-up – the weakness is that the spy can monitor access to shared memory lines and consequently infer information about the data the victim processes

## Slide 29: Flush+Reload code
mfence
rdtscp
mov %eax, %esi
mov (%ebx), %eax
rdtscp
sub %esi, %eax
clflush 0(%ebx)
Also need:
  Wait
  Data collection
  Noise handling
  Initial parsing

## Slide 30: Demo
FR-1-file-access
FR-2-file-access
FR-threshold

## Slide 31: Finding code
Use nm, gdb, objdump, etc.
  Demo scripts functiondump.sh and debuginfo.sh
Remember the base address

## Slide 32: Demo
FR-function-call

## Slide 33: A closer look at F+R
Time
flush
wait wait wait wait
Reload
flush
wait wait wait wait
Reload
flush
wait wait wait

## Slide 34: A closer look at F+R
Time
flush
wait wait wait wait
Reload
flush
wait wait wait wait
flush
wait wait wait
Spy
Victim
working working
working working
access

## Slide 35: Timing matters
Time
flush
wait wait wait wait
Reload
flush
wait wait wait wait
flush
wait wait wait
Spy
Victim
working working
working working
access
Reload
Access missed due to temporal overlap

## Slide 36: Demo
FR-function-call-nodelay

## Slide 37: Probability of a probe miss [ABF+15]
Ratio of wait time to slot length

## Slide 38: Handling misses
Probe function calls [YB14]
  A cache line containing a function call is accessed once before the call and once on return
    Except, maybe, when the return address is in the next cache line
  The timings of the two accesses are not independent
Probe loops [YF14]

## Slide 39: GnuPG 1.4.13 Modular Exponentiation
x ⟵1
for i ⟵|e|-1 downto 0 do
x ⟵x2 mod n
if (ei =1) then
x = xb mod n
endif
done
return x
Example:
115 mod 100 =
161,051 mod 100 = 51
Operation | res | i | ei
 | 1 | 2 | 101
Square | 1 | 2 | 101
reduce | 1 | 2 | 101
Multiply | 11 | 2 | 101
reduce | 11 | 2 | 101
Square | 121 | 1 | 101
reduce | 21 | 1 | 101
Square | 441 | 0 | 101
reduce | 41 | 0 | 101
Multiply | 451 | 0 | 101
reduce | 51 | 0 | 101
The secret exponent is encoded in the sequence of operations !!!
Notes: Stress secret key

## Slide 40: Demo
FR-gnupg-1.4.13

## Slide 41: F+R Spatial Resolution
Cache line
  Can't have two different probes on the same cache line
Cache line pairs
  Probes on paired lines interfere with each other –Don't
Streaming
  Use "random" order when probing multiple lines in the same page
  Don't probe too many of those
Speculative execution
  Probe rear end of functions

## Slide 42: Improving temporal resolution
Scheduler trick [GBK11]
  Monitoring each and every memory access
  Requires hyperthreadings
  Uses hundreds of threads
Amplification [ABF+15]
  Flushing commonly used cache lines slows the victim

## Slide 43: Demo
FR-flush

## Slide 44: Flush+Reload Summary
Simple attack
  Even without Mastik
High temporal resolution
  Up to sub-micro-second
High accuracy
  Few false positives
    Increases as a function of spatial granularity
  A bit more false negatives
    Particularly when exploiting the high temporal resolution

## Slide 45: Variants
Evict+Reload [GSM15]
  Uses cache contention instead of clflush
Flush+Flush [GMWM16]
  Measures variations in clflush timing between cached and non-cached data
  Improved temporal and spatial resolution
  Increased error rate
Invalidate+Transfer [IES16]
  Use Flush+Reload on Intel or Evict+Reload on ARM to implement a cross-package attack
Flush+Reload on ARM [ZXZ16]
  ???